## Slide 1: Data processing and data management for a neutrino telescope
Mieke Bouwhuis (KM3NeT / NIKHEF)
31 March 2022

## Slide 2: The KM3NeT Neutrino Telescope
Distributed infrastructure in the Mediterranean Sea
  FR: 107 m3
  IT: 1 km3
Modular telescope array
  345 vertical strings
  200.000 light-sensitive photo-multiplier tubes
Today:
  FR: 10% operational
  IT: 5% operational

## Slide 3: KM3NeT data rates
Detection of Cherenkov light produced by relativistic particles
Photo-multiplier tubes (PMT) measure the arrival time of the light at the quantum level
PMT singles rate 10 kHz
1 string 300 Mbps
Full detector 100 Gbps (345 strings)
18 modules/string
31 PMTs/module
All data to shore

## Slide 4: KM3NeT Computing Model
CC-FR
CC-IT
FR
IT
onshore computing
onshore computing
Tier-0
Tier-1
Tier-2
data
acquisition
data
processing
data
analysis
data
storage
CC-FR
CC-IT
Computer Centre FR
Computer Centre IT
Computer Centre PL
Computer Centre NL
Computer Centre …
Local computing resources

## Slide 5: Using DIOS in KM3NeT
FR
IT
onshore computing
onshore computing
Tier-0
Tier-1
Tier-2
data
acquisition
data
processing
data
analysis
data
storage
Local computing resources

## Slide 6: DIOS at the KM3NeT Tier-0 level
onshore computing
All data to shore
Onshore computing: finding causalities between
  Arrival time of the photons
  Positions of the detection modules
Filters out “events”
  Event rate: 200 Hz
  Reduction factor: 104
DIOS handles data storage of filtered events
  Safe storage
  Replication to multiple sites
“events”

## Slide 7: DIOS at the KM3NeT Tier-1 level
Calibration of raw events
  PMT quantum efficiency calibration
  PMT gain calibration
  Position calibration of detection modules
  Orientation calibration of detection modules
  ….
“Reconstruction” of calibrated events, determination of
  neutrino type
  neutrino direction
  neutrino energy
DIOS handles storage of calibrated and reconstructed data
  Accessible to all KM3NeT partners
  Distribution of the data processing
  Organization in data sets
raw events
reconstructed events
Input to all analyses

## Slide 8: DIOS at the KM3NeT Tier-2 level
Scientific analyses
  Neutrino astronomy
  Multi-messenger astronomy
Usage of single interface Data Lake as a Service
  Finding calibrated and reconstructed data
  Conversion to reduced data format
  Ingestion into the Data Lake
Data Lake as a Service experience
  User-friendly interface to the Data Lake
  Organization in data sets
  Integrated development environment

## Slide 9: Conclusions
KM3NeT under construction
  Data taking ongoing 24/7
  Analyses progressing
Different data processing at different data levels
KM3NeT needs a data management solution for the next 15-20 years
Demonstrated KM3NeT with DIOS on all data management layers
KM3NeT is adopting a DIOS-like infrastructure